## Slide 1: How to build a better testbed
Fabien Hermenier
Robert Ricci
Lessons From a Decade of Network Experiments on Emulab
TridentCom’ 2012

## Slide 2: Network testbeds
support for experiments in networked systems
highly customizable networked environments
raw access to a variety of specific hardware
design and features to match researchers’ needs

## Slide 3: Testbed physical design
no extensive studies for effective testbed design
  assumption-based
  budget-constrained
lack of data from real experimenters
bad design decisions have consequences
  prevent support for certain experiments
  over-commitment on un-needed hardware
Notes: PHYSICAL DESIGN
PHYSICAL
PHYSICAL

## Slide 4: How to build better testbeds ?
careful analysis of the Utah Emulab facility usage
  one of the largest testbeds
  used in production since 2001
  > 4 dozen testbeds worldwide with a similar designs
several alternative testbed designs
evaluation of new designs using real workload
Notes: - Carefully analysis the usage of the testbed
Several alternative testbed design
Evaluate
Conclusions
Then the “small” points

## Slide 5: The Utah Emulab facility: not just another pretty cluster
Notes: One it is big enough, multiple switches, bisection bandwidth dilemma

## Slide 6: Virtual topology in Emulab
Lan node
Full bisection bandwidth between members
Traffic shaping
Implemented with a PC “delay node”

## Slide 7: Making the virtual into reality

## Slide 8: Mapping a virtual topology

## Slide 9: The raw dataset
522 projects – 22,266 experiments – 619,504 topologies
empty, non-instantiated and single node topologies
unconnected topologies
internal projects
- non-cluster resources
The working dataset
477 projects – 13,057 experiments – 504,226 topologies

## Slide 10: Most experiments are small
80%
4%
multiplexable topologies
  to increase acceptance rate
  to deploy larger experiments
prepare with small topologies
evaluate with larger

## Slide 11: Attractive nodes are the bottleneck
upgrading is a necessity
  to meet the demand
  to support larger experiments
beauty is ephemeral
repeatability is essential
Notes: REMOVE shade, increase dot line size
Back to colors
Recent nodes instead of pc3000/d710
Emphaze old node or the nodes I am talking about during the talk

## Slide 12: Most requests use few interfaces
network interfaces are wasted
homogeneous connectivity does not reflect the reality of usage
traffic shaping is a prime feature
multiple interfaces are required

## Slide 13: LANs are common, but most are small
another prime feature
LANs dominate large experiments
90%
small LANs
a moderated usage of the interswitch bandwidth ?
Notes: Change the color of the dashes

## Slide 14: Facts from experimenters data
the testbed size limits
  its acceptance rate
  experiments size
connectivity is overprovisioned
improved designs must provide
  some nodes with multiple interfaces
  non-blocking bandwidth between a few nodes

## Slide 15: A cost model for testbeds
the impact of high connectivity is significant at scale
  $100,000: 34 2-link nodes or 27 4-link nodes ?
  $1,000,000: 370 2-link nodes or 270 4-link nodes ?
Notes: Be more explicit about Emulab. Show the logo after to be forced to talk about Emulab
Change the colors

## Slide 16: Heterogeneous node connectivity
the best nodes for a topology do not have extra links
from an ideal node connectivity distribution…
… to a testbed that minimizes link waste
+25%

## Slide 17: A cost model for testbeds
small switches lead to a 30% bigger testbed …
… but the reduced bisection bandwidth between the nodes limits maximum LAN size

## Slide 18: The interswitch bandwidth myth
a simulation replayed the user requests for the pc3000 nodes
interswitch links are overprovisioned
an opportunity for smaller and cheaper switches
Busted
97% of the topologies

## Slide 19: Alternative for switch connectivity
interswitch bandwidth
  limit LANs, experiments among switches
faster interconnect are expensive
link concentration limits direct communication
Notes: Visual help to understand
Spend some time to explain
- Talk about the testbed, then the mapping.
1- Only the switches,
2- Add the nodes to show the concentration
Next: more nodes connected to a same switch

## Slide 20: Striping links
direct communication between nodes
scalability limited by switch size
hard to mix with heterogeneous connectivity

## Slide 21: Evaluating new designs
impact of relevant testbed designs on
  completion time
  rejection rate
the cost model as a testbed generator
the 15k topologies focusing pc3000 nodes as workload
a simulator to replay the mapping
  FIFO scheduling policy
  each topology runs for a day

## Slide 22: Connectivity for nodes: good trade
2-link nodes | Nodes | Bandwidth | Rejections | Time (days)
0% | 130 | 1.46 Gb | 0 | 1564
60% | 148 | 1.11 Gb | 0 | 1394
90% | 161 | 30 Mb | 33 (0.2%) | 1487
Testbeds
  $500,000 as funds
  nodes with 2 or 4 links
Notes: Make strong conclusions
Just talk about the context, next the title
Popup for the conclusion

## Slide 23: Striping annihilates bandwidth requirements
Configuration | Bandwidth | Rejections | Time (days)
 | 1.11 Gb | 0 | 1394
 | 85 Mb | 0 | 996
Testbeds
  148 nodes; 60% with 2-links
  2 switches

## Slide 24: Small switches, big testbed
Configuration | Cost | Nodes | Bandwidth | Rejections | Time (days)
264-ports | $498,796 | 148 | 1.11 Gb | 0 | 1394
48-ports | $498,354 | 186 | 1.06 Gb | 138 (0.9%) | 996
48-ports | $390,268 | 148 | 883 Mb | 142 (0.9%) | 1314
using large switches, support the 0.9% “hard” topologies
  with 40% more time
  with $108,000. $761 per “hard” topology vs. $33.5
  we are the 99%

## Slide 25: Conclusions
the testbed size is the bottleneck, not the network
facts lead to new design suggestions
  lower connectivity
  smaller switches
  link striping
cost models and replays for a good insight into the testbed’s effectiveness
what to give up to support the outliers?
read the paper for more conclusions
Notes: Split Third sub-bullet
Outliers:
for example … LAN experiment are 20 times more expensive. But experiments may be still relevant. Separated testbeds ?

## Slide 26
Watson, I told you the problem wasn’t
the interswitch bandwidth
#!*$@ you Sherlock
How to Build a Better Testbed Lessons from a decade of network experiments on Emulab

## Slide 27: Datacenter vs. network testbed physical design
datacenters
  node centric
  network as a support to maximize performance
  non-explicit communications
network testbeds
  network centric
  explicit communication to reproduce
  conservative allocation